## Slide 1: WELCOME TO Catching Kowa DSL Training
Network WF

## Slide 2
Connection problem
Notes: Tools used on connection problem ( OTCCT ,

## Slide 3: - To be able to use the internet , customer should configure the router to get IP (internet protocol) . - we have two kinds of configuration type: 1- PPPOE ( Username same as on Siebel ) 2- IPOE ( 8 and 16 Static IP )

## Slide 4: Configuration for dynamic or 1 static customer ( PPPOE ) & ( port forward ) Please refer to the Router devices Pp

## Slide 5: Configuration for 8, 16 static Ips ( Copper ) ( IPOE )

## Slide 9
Please click here :

## Slide 10
For MSAN customer
IPOE

## Slide 11
Authentication

## Slide 12: Authentication
General definition : customer line is physically up with no IP ( internet protocol )

## Slide 13
OCTOPUS Tool
IP tool

## Slide 14: How to open Authentication WF

## Slide 15: Authentication WF

## Slide 16: Authentication WF

## Slide 20
Notes: Check OTCCT tool

## Slide 21
Reset the customer port via FTTH Tool or octopus. ​

## Slide 23
Open SR
تمام يااستاذ\ ة انا قدمت لحضرتك طلب والمشكلة هتكون اتحلت خلال ال 24 ساعه القادمة محتاج حضرتك تسيب الراوتر شغال ولو بعد 24 ساعه المشكلة لسه موجوده ممكن حضرتك تشرفنا بالاتصال مره تانية)

## Slide 24
Notes: في حاله ان العميل بيواجه مشكله Login Failed و ال Username مكتوب غلط علي ال OTCCT لازم ندخل علي صفحة الراوتر و نعدل ال username ولو مش عارفين ندخل علي صفحة الراوتر نعيد تعريفه من البداية .Reconfiguration في حاله انه صحيح و عنده مشكله login failed و ال Inner Vlan او ال Cabinet علي ال FTTH Toolمختلفة بالمقارنة بال OTCCT نكلم ال Assist Hunt .لو المشكلة لسه موجوده نعمل Authentication SR بصوره طبيعية ولو فيه مشكله فال Falcon ال Assist هيوضحلك تعمل ايه بناء علي المشكلة.

## Slide 25: We should match the username on session logs with username on Siebel

## Slide 28: ​​​​​​​​​​​​​​ In case customer has login failed with matched username, call assist hunt (08100) even if customer doesn't have Inner VLAN or Cabinet code mismatch to confirm that there is no mismatch on falcon as well. Compare between Octopus​ & TE-Portal (Cabinet Code & Inner VLAN)
1-If Customer has Cabinet code Miss match
*OCTOPUS
*FTTH Tool

## Slide 29: 2- If Customer has Inner VLAN Mismatch
*OCTOPUS
*FTTH Tool

## Slide 30: 3- No Account on Falcon

## Slide 31: 4- If customer hasn't problem in Cabinet Code or Inner VLAN

## Slide 32
If customer can’t browse and problem isn’t solved so let customer restart the router

## Slide 33
Open SR
تمام يااستاذ\ ة انا قدمت لحضرتك طلب والمشكلة هتكون اتحلت خلال ال 24 ساعه القادمة محتاج حضرتك تسيب الراوتر شغال ولو بعد 24 ساعه المشكلة لسه موجوده ممكن حضرتك تشرفنا بالاتصال مره تانية

## Slide 35
If the cabinet has traffic normally:
​Reset the customer port via TE Portal​ by pressing on "Lock port then Unlock port" ​​for MSAN Lines:

## Slide 37
Open SR
تمام يااستاذ\ ة انا قدمت لحضرتك طلب والمشكلة هتكون اتحلت خلال ال 24 ساعه القادمة محتاج حضرتك تسيب الراوتر شغال ولو بعد 24 ساعه المشكلة لسه موجوده ممكن حضرتك تشرفنا بالاتصال مره تانية

## Slide 38
In case agent was checking the logical connection on Octopus and found the customer has "Connect Issue":
  Agent should open the router's page and modify the username to be same as Siebel username.
  In case solved​​​, agent ​should create the relevant SR and close it with the proper Sub Area.
  If Not Solved, create the relevant SR to be assigned to the concerned team.

## Slide 39
No Browsing
That’s mean customer authenticated with IP ,all router leds are up with right light but he can’t browse all web sites .

## Slide 40: How to open no browsing WF

## Slide 41: No Browsing WF

## Slide 42
We have to confirm that line is up , authenticated and doesn’t have redirection page
Check IP on IP Tool as below
Check if there is any redirection page or not through Siebel as below
Notes: Should check IP tool and PCRF ( QOS and redirection )

## Slide 43
​​​Confirm that the line is physically up, stable & authenticated​​.
Advise the customer to open any browser and type this IP (172.217.23.100).
​
Check which page the customer is directed to:
انا واضح عندي يافندم ان في مشكلة فنية على خط حضرتك.
انا هقدم لحضرتك شكوى وهيتم التواصل مع حضرتك خلال 48 ساعه

## Slide 46
If issue is solved after CPE restart

## Slide 48
Check customer's QOS Profile through PCRF and Connected with IP through IP tool

## Slide 49
If Customer can’t browse, Check customer services type Dynamic IP or 1 Static IP from SRs on Siebel:

## Slide 58
If issue is solved after checking TCP/IP Setting create the below SR

## Slide 59
Try to reset and Re-configure CPE​
You can check router simulation

## Slide 60
If Issue is solved after reset and Re-configure CPE ,create the below SR

## Slide 61
Script:
تمام يا أستاذ/ة....... أنا سجلت الطلب لحضرتك وفي خلال الـ24 ساعة اللي جاية فيه حد هيتواصل مع حضرتك من جانبنا لحل المشكلة ونستأذنك تسيب الراوتر شغال ​.​​​​​​
Short Code | 40013
Type | DSL Fault For Connectivity​
Area | No Browsing​
Product | ADSL
Owner Group | Data Tech Con Support-Network
Sub Area | Empty​
Status | Open
Smart Script | Yes​
SLA | 24 H​​

## Slide 62
In case customer has no browsing while using mobile and doesn’t have PC

## Slide 63
If issue is still existed

## Slide 64
Script:
تمام يا استاذ/ة...... انا قدمت طلب لحضرتك وفي خلال ال 24 ساعه اللي جايه هيتم التواصل مع حضرتك من جانبنا لحل المشكلة الفنية
Short Code | 40013
Type | DSL Fault For Connectivity​
Area | No Browsing​
Product | ADSL
Owner Group | Data Tech Con Support-Network
Sub Area | Empty​
Status | Open
Smart Script | Yes​
SLA | 24 H​​

## Slide 66
If Matched, we will continue the same previous WF steps from the below point
If not Matched

## Slide 67
Script
تمام يااستاذ\ ة انا قدمت لحضرتك طلب والمشكله هتكون اتحلت خلال ال 24 ساعه القادمه محتاج حضرتك تسيب الراوتر شغال ولو بعد 24 ىساعه المشكله لسه موجوده ممكن حضرتك تشرفنا بالاتصال مره تانيه
​

## Slide 68
Check customer's QOS Profile through PCRF and Connected with IP through IP tool

## Slide 70
Check customer's QOS Profile through PCRF and Connected with IP through IP tool

## Slide 71
Redirection Page

## Slide 73
​List of redirections that the action will be taken through SRs:
  Redirection Activation: Related SR (3102)
  Redirection Suspension: Related SR (3104)
  Redirection No payment: Related SR (3100)
  Redirection Unknown : Related SR (3101 )
  Redirection Cancelation: Related SR (3103)​
​​Important Notes:
  In case of Active Account: SR should be assigned to DSL CH VAS​.
  In case of Candidate Account: SR should be assigned to DSL Installation Team as below 2 scenarios:
    New activation.
    Change user name or connectivity.​
Redirect_Activation :
  Check if the customer has ( New Activation order ) , check if the self installation task is still pending , configure the CPE with customer and then activate the service via ( aa.com ) ( 172.217.23.110 )​, or (74.125.133.113 ) by asking the customer to press on activate option and if he already configured his CPE proceed on activation step , finally recheck if self installation task is closed automatically or not , call Assist Hunt to close if customer did all these steps and Order is completed but still has redirect activation Create SR (3102)

## Slide 74
Redirect_Suspension ​:
If the customer has Voluntary Suspension order ​ ​​>> Advise him how to reactivate the Service
If the Customer has Modify Service order ​>> Check the pending Task and handle it
If the Customer doesn't have Pending order , Create SR (3104)
Redirect​ No Payment :
In case of receiving customer's complaint from “No browsing" issue and after checking agent found that account has due amount.
Agent should check if the customer has due bill and exceeded the grace period or not.
If yes, Advise the customer to pay his/her due amount and Create Release Line SR if eligible (promise to pay).
If no, and still has redirect No Payment ,OR , if release line SR is submitted​ but still has redirect No payment create the below relevant SR "3100".

## Slide 75
Redirect​ Cancellation :
Check if the customer has "Deactivate Service Request", if yes, follow cancellation WF.
If No, or there is "Deactivate Service Request" and its status is cancelled but customer still has redirect cancellation , create the below relevant SR “3103”.
Redirect​ Unknown_User :
Redirection Unknown User only happens in one of the below scenarios:
  New Activation request.
  Change Username request.
Accordingly, agent should ensure that customer is configured with the same username as Siebel (compare the username which exists on Octopus Log with
Siebel Username) and if not modify it from router’s page.
If username is correct , create the below relevant SR “3101”.

## Slide 76
Slow Download

## Slide 77
How to open Slow Download WF

## Slide 79
Slow Download could be considered as Physical or network issue
*For MSAN (check from TE-Portal)
Check first pervious SRs and related comments to avoid wrong SR .
Bad line in MSAN to considered bad if the MAX is less 36 maintaining that the port and router are VDSL.
Bad line is considered if line is less than 15 M for customers with ADSL port or ADSL router.​
For Copper (check from Octopus​)
  Relative Occupation : < 85%
  Noise Margin : > 60 dB
  Signal Att : < 350 dB
  Bitrate : < 85% from the Max rate
  Max att : > 6144 kb/s​
It is considered as network issue if the parameters are good so if customer has problem in QOS , Bit rate , or if every thing is ok but he still has slow , it will be handled as network issue
Physical issues requires to check , splitter wiring , internal wiring , Box and cabinet to be solved
We must make sure that customer didn’t consume all his Quota and his speed isn’t downgraded to 256 K
We must make sure that customer got right QOS matched with his speed

## Slide 80
QOS
Check customer’s quota consumption through Siebel PCRF as shown below if the package is fully consumed or not.
If not fully consumed, follow the below troubleshooting steps.
If fully consumed, offer upgrading the package/adding extension using the below script and create & close the below SR.

## Slide 81
Normal QOS

## Slide 84
- Check customer quota consumption and make sure that he didn’t consume all his Quota​
Notes: PCRF

## Slide 85
Check line parameters to determine if they are good or not
For copper we will check parameters through OCTOPUS

## Slide 86
For MSAN through FTTH Tool

## Slide 88
* For Copper
*For MSAN

## Slide 91
Open SR
تمام يا أستاذ/ة....... أنا سجلت طلب حضرتك وفى حد من الدعم الفني هيتابع الشكوى، بستأذن حضرتك نسيب الراوتر متوصل، ولو مفيش أي تأخير من المصرية للاتصالات في خلال 48 ساعة عمل هتكون الخدمة شغاله بصوره طبيعية عند حضرتك
Sort code 39013
Type DSL Fault For Physical
Area Bad Line
Product ADSL
Smart Script Yes
Owner Group Data Tech Con Support-Physical
Sub Area Empty
Status Open
SLA 48 WH

## Slide 92
To determine if customer has bitrate Mismatch or not check the following :
Relative Occupation should be less than 85% ( Relative Occupation = Current Rate / Max attainable Rate )
Example 1 :
If the Max Attainable Rate is 20480 , the Bitrate should be less than 85% from 20480 (Current Rate 16384)
We will divide Current Rate / Max Attainable Rate ) 16384/20480 = 80 % >>> doesn't have Bit rate Mismatch
Example 2:
If the Max Attainable Rate is 20480 , the Bitrate should be less than 85% from 20480 (Current Rate 10240)
We will divide Current Rate / Max Attainable Rate ) 10240/20480 = 50% >>> has Bit rate Mismatch​

## Slide 93
If parameters are good , Check Bit Rate on OCTOPUS for copper or FTTH Tool for MSAN
Notes: And check QOS on PCRF

## Slide 94
For Copper :
For MSAN :

## Slide 96
Check Bit Rate on OTCCT for copper or FTTH Tool for MSAN

## Slide 97
Notes: Copy the DSLAM Name from OTCCT ( check tool guide )

## Slide 99
​​​•​​In case customer is facing a slowness for any gaming consoles, agent should follow Online Gaming Handling.
In case customer is facing a slowness related to (computers & mobiles) devices, we will follow the below handling:​
Agent will guid​e the customer to open http://www.speedtest.net/.
Ask customer to connect the device with LAN if available.
If not, ask customer to connect through Wi-Fi with 1 device only and disconnect all the others . ​
Check speed test result and compare it with customer’s speed with minimum accepted download speed.
Notes: في حاله ان العميل عنده مشكلة بطء في السرعة وكل القرايات علي السيستم سليمه و عنده جيجات متاحه ( (Quota بنخلي العميل يفتح www.speedtest.net لو علي موبايل هيطلب منه ينزل application بضغط علي GO وبعدها يبيدا يظهر معدل التنزيل و التحميل عند العميل. بتأكد ان معدل السرعة اللي ظاهر للعميل يساوي او اكثر من 65% من ال current rate مش من سرعة العميل لان دي سرعات تصل الي علي حسب كفاءة الخط.
لو العميل نحاس اللي ظاهر للعميل يساوي او اكثر من 45% من ال current rate.

## Slide 101
​In case both minimum speed download rate and speed test results are matched:
  Agent will inform the customer that no problem found.
In case speed download rate is not matched with speed test results:
  A complaint will be submitted.
In case customer refused the Speed Test troubleshooting or wasn't convinced with the Speed Test result:
  ​Agent will follow the normal handling “trusted sites" to test the download rate by informing the customer to download files from trusted sites therefore s/he can compare his/her download rate with the speed test rate.
​Example:
  If the customer's line profile through TE Portal is 16 Mbps, make a speed test and get the accepted rate by applying the below calculation:
  (16384x0.65=10.4)
  If customer refused the speed test troubleshooting or wasn't convinced with the speed test result, agent will follow the normal handling “trusted sites” to test the download rate by (16384x0.65/8).
  If the result is 1331.2 KB/Sec, then it’s accepted.
  If the result is less than 1331.2 KB/Sec, then it's not accepted.

## Slide 102
​​​

## Slide 104
​​- Create SR (SLA 24 H)​

## Slide 105
•​​In case customer is facing a slowness for any gaming consoles, agent should follow Online Gaming Handling.
In case customer is facing a slowness related to (computers & mobiles) devices, we will follow the below handling:​
Agent will guid​e the customer to open http://www.speedtest.net/.
Ask customer to connect the device with LAN if available.
If not, ask customer to connect through Wi-Fi with 1 device only and disconnect all the others . ​
Check speed test result and compare it with customer’s speed with minimum accepted download speed.

## Slide 107
In case both minimum speed download rate and speed test results are matched:
  Agent will inform the customer that no problem found.
In case speed download rate is not matched with speed test results:
  A complaint will be submitted.
In case customer refused the Speed Test troubleshooting or wasn't convinced with the Speed Test result:
  ​Agent will follow the normal handling “trusted sites" to test the download rate by informing the customer to download files from trusted sites therefore s/he can compare his/her download rate with the speed test rate.
Example:
  If the customer's line profile through TE Portal is 16 Mbps, make a speed test and get the accepted rate by applying the below calculation:
  (16384x0.65=10.4)
  If customer refused the speed test troubleshooting or wasn't convinced with the speed test result, agent will follow the normal handling “trusted sites” to test the download rate by (16384x0.65/8).
  If the result is 1331.2 KB/Sec, then it’s accepted.
  If the result is less than 1331.2 KB/Sec, then it's not accepted.

## Slide 109
​​- Create SR (SLA 24 H)​

## Slide 110
Slow Upload
Slow Upload could be considered as Physical or network issue.

## Slide 111
How to Open Slow Upload WF

## Slide 112
1
2

## Slide 114
Check Physical Line parameters from OCTOPUS for copper ​​

## Slide 115
Check Physical Line parameters from FTTH Tool for MSAN
We should check Maximum attainable Rate US ​​

## Slide 116
For Copper :
For MSAN :

## Slide 120
Compare between Bit Rate and Max Attainable rate , Bit Rate should be 65% of Max Attainable Rate ​

## Slide 121
For MSAN :
For Copper :

## Slide 122
Open SR
Script
تمام يااستاذ\ ة انا قدمت لحضرتك طلب والمشكلة هتكون اتحلت خلال ال 24 ساعه القادمة محتاج حضرتك تسيب الراوتر شغال ولو بعد 24 ساعه المشكلة لسه موجوده ممكن حضرتك تشرفنا بالاتصال مره تانيه
Create the below SR & Clarify in SR Note that customer has bit rate mismatch regarding upload speed

## Slide 124
Incase receiving customers subscribed on Up to 30 packages and complaining from his/her upload speed and the reason to be 1 Mbps and instead of 3 Mbps , use the below Script.
​Check customer's package and calculate the accepted upload rate which should be 65% of the current rate.

## Slide 125
Open SR
Script
تمام يااستاذ\ ة انا قدمت لحضرتك طلب والمشكلة هتكون اتحلت خلال ال 24 ساعه القادمة محتاج حضرتك تسيب الراوتر شغال ولو بعد 24 ساعه المشكلة لسه موجوده ممكن حضرتك تشرفنا بالاتصال مره تانيه

## Slide 126
Slow Browsing
Please check customer quota consumption and make sure that he didn’t consume all his usage first before handle slow workflow
Slow browsing could be considered as Physical or network issue.

## Slide 127
How to Open Slow Browsing WF

## Slide 128
1
2

## Slide 130
Before checking Slow browsing we should make sure download rate is accepted
- Use Slow Download Work Flow in case download rate is not accepted ​.
Notes: Check the customer parameters from your side

## Slide 131
Please check customer quota consumption and make sure that he didn’t consume all his usage first before handle slow workflow.
Check Physical Line parameters from Octopus ​for copper.

## Slide 133
Reset the customer’s Browser and check the browsing again, steps will be according to browser type
​Click the Tools "menu".
Select Options.
Click the Under the Hood tab then click on "Clear browsing data" button
Select "the beginning of time" , Mark the needed checkboxes and click "Clear browsing data" button
Click on "Under the Hood" again then click on "Change proxy settings" button
Select Connections tab and make sure the Dial-up Box is Empty then click "LAN settings" button then click "OK" button
Make sure to clear check boxes then click ok

## Slide 135
​​Change the MTU on the customer Modem to 1420
If not solved, agent can try 1300 or 1380 (As an extra mile and not a mandatory step).​
Check Browsing Speed again. ​

## Slide 136
Open SR
​تمام يا أستاذ/ة....... أنا سجلت الطلب وبستأذن حضرتك نسيب الراوتر متوصل وفي خلال الـ 24 ساعه اللي جاية هتكون الخدمة شغالة بصورة طبيعية وفى حاله ان حضرتك واجهت نفس المشكله بعد 24 ساعه ممكن تعاود الاتصال بينا مرة تانية
​​In case of exceeding the SLA:​
​​هقدم لحضرتك طلب استعجال وهيتم الرد في اسرع وقت ممكن.. شكرا لتفهمك ​
​
In case customer using smart phone, open case with the below details and inform him/her to prepare a device connected with cable or WiFi if possible for follow up call.
Inform the customer to keep the CPE connected during the next 24 Hrs.
tScript

## Slide 138
* For Copper
*For MSAN

## Slide 139
- If the customer is calling from DSL service number:
• Ask the customer for his/her mobile number
• Ask customer to end call with you and ask him to answer the call on his/her mobile.
• Put Not Ready
• Call the customer
• Connect with him/her without splitter

## Slide 140
Open SR
تمام يا أستاذ/ة....... أنا سجلت طلب حضرتك وفى حد من الدعم الفني هيتابع الشكوى، بستأذن حضرتك نسيب الراوتر متوصل، ولو مفيش أي تأخير من المصرية للاتصالات في خلال 48 ساعة عمل هتكون الخدمة شغاله بصوره طبيعية عند حضرتك

## Slide 141
Connection Unstable
Not matched physical with logical up time on FTTH Tool & IP Tool
Notes: Connection Unstable Means: the customer has instability connectively (the customer get IP and change it without restarting the router.

## Slide 142
How to Open Connection unstable WF

## Slide 143
2.Open IP Tool and check the login date.
1.​​Open FTTH Tool and check the Port Up time.

## Slide 144
3. If both not matched (the time between port up time & IP and found more than 5 minutes) will assign "40012" Siebel SR to L3 --> Agent shouldn’t do port reset or restart the router​.
Notes: If matched Follow line unstable WF.

## Slide 145
For Copper
IP Tool

## Slide 146
Open SR
3. If both not matched (the time between port up time & IP and found more than 5 minutes) will assign "40012" Siebel SR to L3 --> Agent shouldn’t do port reset or restart the router​.

## Slide 147
Browsing Sites Problem
In case receiving customer complaining from sites problem.
Notes: Browsing sites Problem means: the customer can use internet normally except specific web site or sites

## Slide 148
Customer should have a PC/Laptop in order to follow this handling.
If no and customer only has a mobile, accordingly agent should make sure that the customer is connected (Authenticated and has IP) and date & time is updated.
Agent should create & close the below SR:

## Slide 149
In case can browse other websites, agent should ask the customer If s/he installed a firewall/ ISA server.
If Yes, ask the customer to connect back to back and make sure the default GW for his/her PC/Laptop is router IP (not ISA server IP).
If No, follow the below:​

## Slide 151
- Reset browser settings to default
Let Customer try to open the web site​

## Slide 152
- Check DNS , on TCP/IP Setting​
- Preferred DNS 41.128.225.225
- Alternate DNS 41.128.225.226
1
2
3

## Slide 153
4
5

## Slide 154
Let customer try to open the web site​
6

## Slide 156
Script
تمام يا أستاذ/ة....... أنا سجلت الطلب لحضرتك وفي خلال الـ24 ساعة اللي جاية فيه حد هيتواصل مع حضرتك من جانبنا لحل المشكلة ونستأذنك تسيب الراوتر شغال ​.

## Slide 157
WLAN
Wireless LAN that uses to link more devices using wireless communication from a local area network within limited area.

## Slide 158
How to Open WLAN WF

## Slide 159
1
2

## Slide 160
  How to check if Wireless Installed driver card is installed on windows 10:
    Start button
    Settings
    Network & Internet
    Status
    Network and Sharing Center
    Click on change adapter settings it'll direct you to network connections.
    You notice Wi-Fi icon, if not found that means Wireless network adapter is not installed.
How to check if Wireless Installed driver card is installed on windows 8:​
  ​​From the start menu click on "Desktop" icon

## Slide 164
Wireless Network Card not installed
Installed
Not Installed

## Slide 165
Installed
Not Installed

## Slide 200
(Customer couldn’t find network The same steps Follow WF customer found his network

## Slide 207
That’s mean there is PC problem

## Slide 220
Quota Problems

## Slide 221
Notes: Check PCRF

## Slide 222
How to Open Quota Consumption Issues WF

## Slide 224
No limitation for recharging quota, Our customer can recharge unlimited count of quota.
Extra validity is 1 month.​
Recharge options are (16333 & shops & portal ) available for all customer base including GOV customer.

## Slide 225
Check customer balance and his renewal date for his quota (Quota Renewal date = Due Date for invoices)
-Renewal takes place from 12:00 AM till 3:00AM , accordingly no need for escalation during this time.​

## Slide 226
​

## Slide 229
Open SR
تمام يا أستاذ/ة....... أنا سجلت الطلب لحضرتك وفي خلال الـ48 ساعة اللي جاية هنقوم بحل مشكلة حضرتك، وفى حاله ان حضرتك واجهت نفس المشكلة بعد 48 ساعه ممكن تعاود الاتصال بينا مرة تانية
Short Code | 37014
Type | Fault For VAS
Area | Quota Renewal Problem
Product | ADSL
Owner Group | DSL CH VAS​
Sub Area | Empty
Status | Open
Smart Script | Yes

## Slide 231
- Customer complains that he charged (Online or shop or 16333) but he didn’t get extra quota for charging Extra Quota problems through 16333 for charging Extra Quota problems through 16333 Click here​
- Check on PGW (Payment Gateway) if transaction done successfully.
2
1

## Slide 232
Customer complains that he charged (Online or shop or 16333) but he didn’t get extra quota
- Check on PGW (Payment Gateway) if transaction done successfully

## Slide 233
If Transaction done successfully on PGW (Payment Gateway ​and Pay Station), Check Quota on PCRF, if still not updated:
In case customer added extra quota through IVR/Portal/My Orange App but it's duplicated in PCRF Or:
In case customer added 1 or more extra quota by mistake and complained from non-usage due to the new validity or any other reason:
  ​Agent should validate and confirm customer 0 consumption of the claimed extra quota through PCRF.
  ​Agent should create "37021" SR to be assigned to CH Billing​ in order to assign the SR to IT DSL team to remove the extra added Quota from PCRF.
  Then CH Billing agent should adjust the customer's balance accordingly including the VAT.

## Slide 235
Make sure to fill the below data in the Smart Script:
Last 4 digits from credit card
Amount
Transaction date
Channel ( my orange App or through portal)
Add note: it is for bill payment or purchasing extra quota
Number used for access the application
Contact number​
Note : Don't forget to attach the reference from PGW in the SR .
Don't open the SR before passing 24 hours from extra quota purchasing date.
Taking into consideration that in case customer purchased the extra quota from shop, the payment receipt should be attached.
Make sure to mention all the payment details within the Smart script.

## Slide 238
-This Scenario occurs when quota consumption doesn't count (consumption not updated)
- Check PCRF and verify we Will notice that there is normal usage appears in the daily usage on PCRF while remaining quota isn’t decreased

## Slide 239
Open SR
تمام يا أستاذ/ة....... أنا سجلت الطلب لحضرتك وفي خلال الـ48 ساعة اللي جاية هنقوم بحل مشكلة حضرتك، وفى حاله ان حضرتك واجهت نفس المشكلة بعد 48 ساعه ممكن تعاود الاتصال بينا مرة تانية
Short Code | 37004
Type | Fault For VAS
Area | Quota Dispute
Product | Choose Customer's package​
Owner Group | DSL CH VAS​
Sub Area | Empty
Status | Open
Smart Script | Yes
-This Scenario occurs when quota consumption doesn't count (consumption not updated)
- Check PCRF and verify​, if the error found:

## Slide 240
-This Scenario occurs when quota consumption doesn't count (consumption not updated)
- Check PCRF and verify​, if there's no error close the below SR .
​

## Slide 241
Online Gaming support
Could be considered as Physical or network issue.

## Slide 242
How to Open Quota Consumption Issues WF

## Slide 246
Thank you
Thank you